RS485
- Serial Communication
- Nr of Nodes >= 2
- No automatic access mechanism’s
  - Easy to get collision between messages
- A node read what it is transmitting
  - Meaning TX and RX channels 100% separated logic wise

---
RS485-II
- TX is a “double signal”
- Receiver is differential so receive a “0” or “1” is not an absolute voltage
- But rather “positive” or negative”

---
Noise immunity
- Twisted cables and ...
- Differential signals
- “makes” cables longer :-)

---
How long ? How many ?
- RS422 is a differential variant of rs232
- 120 ohm terminating resistors is tp avoid standing waves on the cables
- No of nodes is restricted by “fanout” - how much a TX nodes can “produce” og amperes on the cable
- Length normally < 1200m (rs232 < 15m)

---
How ?
- Default in RX-only mode
- Activate TX circuit by “RTS” Request To Send
- NB: Arduinos TX with 0-5V signals
- The rs485 interface convert it to symmetric

---
Access to rs485 network – Ostrich protocol
- Ostrich method
  - Go for it just ...
  - Activate your rs485 tx
  - Send your bits and bytes
  - Deactivate your rs485 tx
- You might be lucky
- Or have message collision == you loose your data
- Open question(s)
  - How do you detect message loss ?
  - What will you do upon detection ?

---
Media Access Policy
- RS485 has no builtin (hardware) mechanism
- You will do design your own access protocol
- ...

---
Media Access Policy
- RS485 has no builtin (hardware) mechanism
- You will do design your own access protocol
- The next simples (Ostrich is the simplest)
- Master slave(s) policy
- Only master can initiate communication
- Its convenient that all slave nodes has a known identity
- Slaves will reply upon request from master
- Master can initiate
  - Tx data to slave(s)
  - Request to slave to TX data back to master
- In basic version it’s a little uphill (performancewise) to move data
  - From one slave to another slave
  - -

---
Protocols – here the problems starts
1. Master asks slave A to send data to master
2. Master sends slave As data to slave B which need it
Potential problems
1. A slave has some important info that it “need” to deliver now
  1. What is now ?
  2. The slave has to wait on the master requesting for info
  3. When will thois happen ?
  4. Its up to the master
So you have to design a protocol which
- Takes care of timing in your system
- On regular(?!) intervals ask relevant slaves for “new news”
Regular cyclic executive systems are well suited because
You can design a master driven cyclic service scheme for the slaves

---
Dynamixel
- Two protocols:
  - Protocol 1
  - Protocol 2 (love the names)

---
Instructions field

---
Add parameters and CRC-16 check
- Th CRC-16 field is to ensure that the intended receiver receives an ok pkg
- There is a broadcast address (0xfe) so you can contact all
  - For reset etc

---
Example: status Pkg
All Dynamixels motors has some command id for status: 0x55

---
Your setup
- An arduino or eq
- A rs485 net
- Mx motors on the rs485 net
- So tx/rx code as normal but with surrounding “activate/deactivate interface”

---
XBEE

---
One way communication
- Measuring devices sends messages on regular intervals
- Only one type of message
  - 2 analog EMG 16 bit int measurements
  - 3 analog accelerometer x,y,z 16 bit int measurements
  - A simple checksum
  - http://kom.aau.dk/~jdn/edu/courses/19-2/sensact/xbee.html

---
Short about time – cyclic executive
- Given ...
  - No kernel or operating system
  - Nothing to do except for the regulary executive

---
unsigned long tt=1000; // 100 msec executive
unsigned long t1;
void setup() {
  // put your setup code here, to run once:
Serial.begin(9600);
  t1=millis(); // init
}
boolean isItTime()
{
  unsigned long t;
  t = millis();
  if (tt <= t- t1) {
    t1 = t;
    return true;
  }
  else { return false; }
}
void doYourCode()
{
Serial.println(t1);
delay (random(200,600));
}
void loop() {
  while (! isItTime()) ;
  doYourCode();
}

---
unsigned long tt=1000;
unsigned long t1;
void setup() {
Serial.begin(9600);
  t1=millis(); // init
}
boolean isItTime()
{
  unsigned long t;
  t = millis();
  if (tt <= t- t1) {
    t1 = t;
    return true;
  }
  else {
    return false;
 }
}
void doYourCode()
{
 Serial.println(t1);
 delay (random(200,600));
}
void loop() {
  while (! isItTime()) ;
  doYourCode();
}

---
Who is who ?
- You are the master
- You shall talk with your nodes/slaves
Time and speed
- Your RS485 is signalwise driven by your Adruino/Teensy/...
- So you have given baudrate ( 1 byte ~= 10 bits)
  - 9600 baud ~= 900 bytes/second
- A protocol pkg is a least 12 bytes and more often 20 bytes
- So @9600 you can TX at most 450 pkg/sec
- An if you need a reply 200 call-reply pkgs – at most !!!
- Welcome to a new world

---
More complicated code
- You might want to have more than one service running
  - A service can be your controller ...
    1. Getting data from your motors (angles, momentuum,...) I assume you are the master
    2. Calculating controller
    3. Tx setpoints back to the motors
    4. Wait until next sample time
- Solutions might be...
- “complicated” intereupt system
- A realtime operating system or kernel
- Not the scope 2day
- 2day – get into communication with your robot with your own code
EOL