Analog to Digital Converter
Denis BISSIERES
Ian CAMPBELL
Yohan LESPERAT
Mechatronics - Fall 04
What is ADC ?
Types of ADCs
HC11 & ADC

---
Contents

---
- Definition
- Examples of use
- Conversion process
- Accuracy

---
Definition
- Most signals we want to process are analog
- i.e.: they are continuous and can take an inifinity of values
x(t)
t

---
Definition
- Digital systems require discrete digital data
- ADC converts an analog information into a digital information
?
Digital System
Digital
Analog

---
Examples of use
Voltmeter
7.77 V
ΔV
Cell phone (microphone)
Wave
Voice

---
Conversion process
3 steps:
- Sampling
- Quantification
- Coding
These operations are all performed in a same element: the A to D Converter

---
Conversion process: Sampling
- Digital system works with discrete states
- The signal is only defined at determined times
- The sampling times are proportional to the sampling period (Ts)
x(t)
xs(t)
Ts
x(t)
xs(t=k*Ts)
t
Ts

---
Conversion process: Quantification
The signal can only take determined values
Belonging to a range of conversion (ΔVr)
- Based on number of bit combinations that the converter can output
- Number of possible states:
N=2n where n is number of bits
Resolution: Q= ΔVr/N
xs(t)
xq(t)
t
Ts
ΔVr
Q

---
Conversion process: Coding
- Assigning a unique digital word to each sample
- Matching the digital word to the input signal
xq(t)
N-1
N-2
2
1
0
t
Ts
ΔVr
Q

---
Accuracy
The accuracy of an ADC can be improved by increasing:
- The sampling rate (Ts)
- The resolution (Q)

---
Accuracy
xq(t)
t
Ts
Q
t
Ts
xq(t)
Higher Sampling rate
t
Q
xq(t)
Higher Resolution

---
Sampling rate
Nyquist-Shannon theorem: Minimum sampling rate should be at least twice the highest data frequency of the analog signal
fs>2*fmax

---
Sampling rate
Analog signals are composed of an infinity of harmonics
Need to limit the frequency band to its useful part
Use of an analog filter
ADC
AnalogFilter
Digital
Analog
Analog
In practice: fs ≈ (3…5)*ffilter

---
Example
8 bits converter: n=8
Range of conversion: ΔVr=5V
Sampling time: Ts=1ms
Number of possible states: N=28=256
Resolution: Q=ΔVr/N=19.5 mV
Analog Filter: ffilter ≈ fs/5 = 200 Hz
5
255
Gain
f
0
0
Analog
Digital

---
- Flash ADC
- Sigma-delta ADC
- Dual slope converter
- Successive approximation converter

---
Flash ADC
- “parallel A/D”
- Uses a series of comparators
- Each comparator compares Vin to a different reference voltage, starting w/ Vref = 1/2 lsb

---
Flash ADC
Comparator is one use of an Op-Amp
If	Output
VIN > VREF	High
VIN < VREF	Low
+
-
VIN
VREF
VOUT

---
Flash ADC
Advantages
Very fast
Disadvantages
- Needs many parts (255 comparators for 8-bit ADC)
- Lower resolution
- Expensive
- Large power consumption

---
Sigma-Delta ADC
- Oversampled input signal goes in the integrator
- Output of integration is compared to GND
- Iterates to produce a serial bitstream
- Output is serial bit stream with # of 1’s proportional to Vin
size 12{ Int {} } {}
Σ
Integrator
Digital
low-pass filter
Sample decimator
Vin
+-
+
1-bit
DAC
-
Oversampler
Serial output

---
Sigma-Delta ADC
Advantages
- High resolution
- No precision external components needed
Disadvantages
Slow due to oversampling

---
Dual Slope converter
Vin
tFIX
tmeas
t
- The sampled signal charges a capacitor for a fixed amount of time
- By integrating over time, noise integrates out of the conversion.
- Then the ADC discharges the capacitor at a fixed rate while a counter counts the ADC's output bits. A longer discharge time results in a higher count.

---
Dual Slope converter
Advantages
Input signal is averaged
Greater noise immunity than other ADC types
High accuracy
Disadvantages
- Slow
- High precision external components required to achieve accuracy

---
Successive Approximation
Is Vin > ½ ADC range?
- Sets MSB
- Converts MSB to analog using DAC
- Compares guess to input
- Set bit
- Test next bit
1000 0000
0100 0000
If no, then test next bit
SAR
DAC
Out
VIN
-
+

---
Successive Approximation
Disadvantages
- Higher resolution successive approximation ADCs will be slower
- Speed limited ~5Msps
Advantages
Capable of high speed
Medium accuracy compared to other ADC types
Good tradeoff between speed and cost

---
ADC Types Comparison
Type	Speed (relative)	Cost (relative)
Dual Slope	Slow	Med
Flash	Very Fast	High
Successive Appox	Medium – Fast	Low
Sigma-Delta	Slow	Low

---
Structure of the acquisition
ADCTL Register
Option Register
Data conversion
Acquistion

---
Structure of the acquisition
Port E (analog input)
8 channels
PE0
AN0
PE1
AN1
PE2
AN2
PE3
AN3
PE4
AN4
PE5
AN5
PE6
AN6
PE7
AN7
ANALOG MUX
8-bits CAPACITIVE DAC WITH SAMPLE AND HOLD
VRH
SUCCESSIVE APPROXIMATION REGISTER AND CONTROL
VRL
INTERNAL DATA BUS
MULT
SCAN
CCF
CD
CC
CB
CA
ADCTL A/D CONTROL
RESULT REGISTER INTERFACE
ADR1
ADR2
ADR3
ADR4
P 64 M68HC11 Family Data Sheet

---
Structure of the acquisition
- 8 channel/bit input
- VRL = 0 volts
- VRH = 5 volts
- Digital input on P
0
1
2
3
4
5
6
7
Port E (analog input)
Analog Multiplexer
A/D Converter
Result Register Interface
ADR1 - result 1
ADR2 - result 2
ADR3 - result 3
ADR4 - result 4

---
ADCTL Register
SCAN
MULT
CD
CC
CB
CA
ADCTL ($1030)
CCF
0
Reset to:	0	0	u	u	u	u	u	u
MULT - Single or multiple channel
0: Sample a single channel (four times)
1: Sample four channels
CD,CC,CB,CA - Channel selection
If MULT is 0, then CC-CA bits specify the channel
If MULT is 1, then CC specifies the group:
0: Sample AN0-AN3, 1: Sample AN4-AN7
CD is reserved for factory test use
CCF - Conversion Complete Flag
Set when all four conversions are complete
Cleared by writing to ADCTL - starts the next conversion
SCAN - Continuous scan mode
0: Take one set of four conversions and stop
1: Continually perform new conversions

---
ADCTL Register
ADR# Behavior
4 channels are continuously converted. ADR1-ADR4 overwritten
One channel is continuously converted. ADR1-ADR4 overwritten
Continuous Conversion
(SCAN = 1)
4 channels converted once. The results are stored in ADR1-ADR4
One channel converted 4 times consecutively. The results are stored in ADR1-ADR4
Single Conversion (SCAN = 0)
Multiple Channel (MULT = 1)
Single Channel
(MULT = 0)

---
Single Channel
7
6
5
4
3
2
1
0
PORT E
ADR1 – Result1
ADR2 – Result2
Result Register Interface
A/D Converter
ADR3 – Result3
ADR4 – Result4

---
Multiple Channels
7
6
5
4
3
2
1
0
PORT E
ADR1 – Result1
ADR2 – Result2
Result Register Interface
A/D Converter
ADR3 – Result3
ADR4 – Result4

---
ADCTL Register
E Clock cycles:
Conversion Sequence
ADCTL write (1)
Sample (12)
Bit 7 (4)
6 (2)
_ (2)
0 (2)
End (2)
Successive approximation
0
32
64
96
128 total
1st, ADR1
2nd, ADR2
3rd, ADR3
4th, ADR4
CCF

---
ADCTL Register
A/D Result Registers (ADR1 – ADR4):
ADR1 = $1031
ADR2 = $1032
ADR3 = $1033
ADR4 = $1034

---
ADCTL Register
A/D Channel Assignment
P447 Reference Manual

---
ADCTL Register
ADR# Behavior
Single Channel	The Channel is selected by CA, CB,
(MULT = 0)	CC
Multiple Channel	The group of Channels is selected by (MULT = A)	CC only

---
Option Register
Options Register ($1039)
ADPU
CSEL
IRQE
DLY
CME
CR1
CR0
ADPU = A/D power up
CSEL = Clock Select
IRQE = Config. IRQ
DLY = Enable start-up delay
CME = Clock Monitor
Bit 2 = not implemented
CR1 = COP Timer Rate
CR2 = COP Timer Rate
Bit:
0
1
4
3
2
6
7
5

---
Option Register
ADPU - A/D Charge Pump
0: Turn off the A/D
1: Turn on the A/D (by enabling the charge pump)
Note: Wait at least 100 microseconds before using the A/D
(This is 200 cycles at a 2MHz E-clock)
CSEL - A/D Clock select
0: Use the E-clock for the A/D
1: Use a special internal A/D clock that runs at around 2MHz
Note: If the E-clock is 750KHz or higher, CSEL should be 0.
Otherwise CSEL should be 1.
DLY – Delay
0 = No delay is used and MCU resumes within approx. 4 cycles.
1 = 4000 E clock cycle delay imposed to allow crystal stabilization

---
Data conversion
size 12{ times 2 rSup { size 8{ - 4} } } {}
size 12{ times 2 rSup { size 8{ - 5} } } {}
size 12{ times 2 rSup { size 8{ - 6} } } {}
size 12{ times 2 rSup { size 8{ - 7} } } {}
size 12{ times 2 rSup { size 8{ - 8} } } {}
size 12{ times 2 rSup { size 8{ - 1} } } {}
size 12{ times 2 rSup { size 8{ - 2} } } {}
size 12{ times 2 rSup { size 8{ - 3} } } {}
(1) %of VRH-VRL, (2) VRH=5 VRL=0, (3) VRH=3.3 VRL=0
Page 41 of the programming reference guide
0.0129
0.0258
0.0516
0.1031
0.2063
0.4125
0.825*
1.65
Volts (3)
0.0195
0.0391
0.0781
0.1562
0.3125
0.625
1.250
2.500
Volts (2)
0.39%
0.78%
1.56%
3.12%
6.25%
12.5%
25%
50%
% (1)
Bit 0
1
2
3
4
5
6
Bit 7

---
Data conversion
MAX :
.1111 1111 = .FF16 = 0.9960937510 = 99.6093 %
Resolution :
.0000 0001 = .0116 = 0.0039062510 = 0.3906 %
MIN :
.0000 0000 = 016 = 010=0 %

---
Data conversion
Some additional notes:
0V <= analog input <= 5V
Charge pump allows VRH max 6-7V
VRL and VRH convert to $00 and $FF
Digital input of Port E pins not recommended during A/D sample time

---
Acquisition
CSEL
OPTION ($1039)
ADPU
IREQ
DLY
CME
0
CR1
CR2
SCAN
CD
CC
CB
CA
CCF
MULT
ADCTL ($1030)
0
OPTION	EQU	$1039
ADCTL	EQU	$1030
ADR1	EQU	$1031
ORG	$1040
LDAA	#$80
STAA	OPTION
LDY	#$411A
NOP
NOP
LOOP	NOP
DEY
BNE	LOOP
LDAA	#$00
STAA	ADCTL
LDX	#ADCTL
WAIT	BRCLR	0,X #$80 WAIT
LDAA	ADR1
PSHA
JSR	$4000
SWI
END
ADPU=1,CSEL=0
Delay for charge pump to stabilize 100µs
SCAN=0,MULT=0,CHAN GRP=00
Wait until CCF or bit 7=“1”
Read and store result

---
Acquisition
Subroutine output to the screen the decimal equivalence of the stack :
ORG	$4000
PULY
PULB
CLRA
LDX	#$000A
IDIV
STAB	$0000
XGDX
LDX	#$000A
IDIV
STAB	$0001
XGDX
TBA
JSR	$FFB5
LDAA	$0001
JSR	$FFB5
LDAA	$0000
JSR	$FFB5
PSHY
RTS
Subroutines Outrhlf, convert to ASCII Number and output to screen
first the hundreds number, the tens and then units number
First Integer Division
Store remainder of the first division
Second Integer Division
Store result to ACCA and remainder to memory of the second division
(NOTE: Remember that ACCA is the high byte of ACCD and ACCB is the low byte of ACCD. Return address used for JSR and RTS is stored in INDEX Y in the subroutine)
A number between 000 and 255 will be print on the screen. If it is 255 -> 100 %
000 -> 0 %

---
Questions ?