Awaiting :-)

---
Sensor/Actuator Communication
by
I2C
- Develop own I2C master slave nodes for
- your own realtime fieldbus
- develop communication scheme
- design & implement master and slaves
- (test timing)

---
http://i2c-bus.org/i2c-primer

---
I2C paradigm
- Master slave communication
  - only master can initiate communication
  - master can write data to slave
  - master can read data from slaves
- Slave cant talk to slave !!!
- Slave cant initiate talk to master !!!
- I2C can do multi master – but out of scope today)
- 100 kHz or 400 kHz

---
I2C electronics (high level is passive

---
Max address i 110xxxx (0-111)
Addresses 111xxxx is used for 10 bit mode etc

---
the Hidden Protocol
- Master and slave need to have negotiated a protocol
- Always:
  - master tells either
  - I will write/Send data to you
  - or
  - I want to receive data from you
- In either case YOU have to define a protocol based on
  - Master always set agenda
  - Slave has to obey
  - Can be simple or complex – it’s up to you

---
 // Wire Master Reader
#include <Wire.h>
void setup() {
  Wire.begin();
  // join i2c bus (address optional for master)
  Serial.begin(9600); // start serial for output
}
void loop() {
// request 1 bytes from slave device #8
  Wire.requestFrom(8, 1);
// slave may send less than requested
  while (Wire.available()) {
    char c = Wire.read();
    Serial.print(c); // print the character
  }
  delay(500);
}
// Wire Slave Sender
#include <Wire.h>
void setup() {
  Wire.begin(8); // join i2c bus with address #8
  Wire.onRequest(requestEvent); // register event
}
void loop() {
  delay(100);
}
// function that executes whenever data is requested
// this function is registered as an event
void requestEvent() {
  // B
  Wire.write(0x42);
  // as expected by master
}

---
Master req 1 byte from slave #8
(get a A 0x14)

---
simple master read protocol
#include <Wire.h>
void setup() {
  Wire.begin(8); // slave addr #8
  Wire.onRequest(requestEvent);
}
void loop() {
  delay(100);
}
// function that executes whenever
// data is requested by master
void requestEvent() {
   Wire.write(“123456”);
   // respond with message of 6 bytes
   // as expected by master
}
#include <Wire.h>
void setup() {
  Wire.begin();         Serial.begin(9600);
}
void loop() {
  Wire.requestFrom(8, 6);
// request 6 bytes from slave #8
  while (Wire.available()) {
  // slave may send less than requested
    char c = Wire.read();
    Serial.print(c);
  }
  delay(500);
}

---
Clock stretching – slave buys time

---
Spec of today mini project
- Two or more Arduinos
  - connect SDA and SCL lines
  - if different power the also connect GND
  - Pullup is integrated Arduino but you might add two 10 kOhms just to be sure

---
a comment
- You cant specify a read address in a read call from master.
- you can only specify id of slave.
- so it’s real simple :-)

---
Slave memory map
- adr 0-3 : “read”	analog read a0-a3
- adr 4-7	: “read”	digital read pin 8,9,10,11
  - initalised as INPUT_PULLUP
- adr 4-7 : “write”	digital write pin 4,5,6,7
  - initalised as OUTPUT
- adr 8	: “write” Serial.print()
- adr 4-7 is used as write and read memory :-)
  - just to save memory map

---
typical read from slave
- master write ID of register to a dedicated register reference register
  - write(<i2c id><reg ref register>< value>)
- and issues a read just after
  - read(<i2c id> <&dest>)
- reg ref register is at adress 39
- we want to read register no 3
char dst;
Wire.”write”<i2c ID>, 39, 3);
Wire.”read”(<i2c UD>, &dst);

---
Spec II
- analog ports at slave	- read only
- digital port at slave	- read and write
- serial port at slave	- write only (Serial.print)

---
write to slave in C
void xxx(char regNo, char *p) {
int i;
 Wire.beginTransmission(DS1307_I2C_ADDRESS);
  Wire.write(regNo);
  for(int i=0; i<length; i++) {
    Wire.write(*p);
    p++;
  }
  Wire.endTransmission();
}

---
slave call back
#include <Wire.h>
void setup() {
  Wire.begin(8); // join i2c bus with address #8
  Wire.onRequest(requestEvent); // register event
}
void loop() {
  delay(100);
}
// function that executes whenever data is requested by master
// this function is registered as an event, see setup()
void requestEvent() {
  Wire.write("hello "); // respond with message of 6 bytes
  // as expected by master
}

---
exercise II – DS 1307 real time clock
- Pick up a DS 1307 and 32 kHz XTAL at lab
- Do the mockup
- Get it up and running
NB at instructables below be aware of how they use
http://www.instructables.com/id/Arduino-Real-Time-Clock-DS1307/

---
DS 1307

---
DS 1307 real time clock(slave addr 0x62)
Simple R/W on all addresses

---
char readASingleByte(char regNo)
{
  Wire.beginTransmission(DS1307_I2C_ADDRESS);
  Wire.write(regNo);
  Wire.endTransmission();
  Wire.requestFrom(DS1307_I2C_ADDRESS, 1);
  return Wire.read();
}
// you can read more than one – its up to you